## Slide 1: Heavy-Hitter Detection on SmatNIC
Yevhenii Liubchyk, Maria Shestakova
Itzik Ashkenazi, Prof. Ori Rotenstreich

## Slide 2: Goal
Track the K heaviest flows with high accuracy using limited available memory.

## Slide 3: Motivation
“Heavy Hitters” flows are flows that contributing significant amounts of traffic to a link.
Detection “heavy hitters” flows is required, for example, for
DoS detection (anomalies and attack)
traffic engineering
relieve link congestion
flow-size aware routing

## Slide 4: Background – Netronome SmartNIC
Agilio CX SmartNIC
Interfaces: 2x10Gb
Processor: NFP-4000
Memory: 2GB

## Slide 5: Background – P4 Language
P4 is a programming language designed to allow programming of packet forwarding planes.
P4 is a domain-specific language with a number of constructs optimized around network data forwarding

## Slide 6: Background – Programmer Studio
Server
Windows
Programmer Studio
P4
Compilation
Netronome SmartNIC

## Slide 7: Overview
Implement HashPipe algorithm on a programmable hardware Netronome SmartNic using P4 language.
Evaluate the accuracy and quality of the algorithm

## Slide 8: HashPipe Algorithm

## Slide 9
P4
vf0_0
vf0_1
Capture file
Memory
Real “Heavy-hitters” flows
HashPipe alg’ flows
Ingress
Traffic

## Slide 10: Code on the Netronome SmartNIC
hh.p4:
hashpipe_algorithm();
modify_field(standard_metadata.egress_spec, port);
plugin.c:
__export __mem static struct Heavy_Hitter sketch[NUM_SKETCH][SKETCH_COLUMN_COUNT];

## Slide 11
P4
vf0_0
vf0_1
Capture file
Memory
Real “Heavy-hitters” flows
HashPipe Alg’
Ingress
Traffic
Egress
Traffic
HashPipe alg’ flows

## Slide 12: Commands
tcpdump – is a type of packet analyzer software utility that monitors and logs TCP/IP traffic passing between a network and the computer on which it is executed.
tcpreplay – is a tool for replaying network traffic from files saved with tcpdump or other tools which write pcap files
nfp_rtsym – Read/write contents of runtime symbol

## Slide 13
P4
vf0_0
vf0_1
Capture file
Memory
Real “Heavy-hitters” flows
HashPipe alg’ flows
HashPipe Alg’
Ingress
Traffic
Egress
Traffic
tcpdump
nfp-rtsym
tcpreplay
Compare:
Accuracy, Errors, Average

## Slide 14: Testing – Input
NUM – number of sending packets
K – number of “heavy-hitter” flows which we want to check
AxBxC – memory size:
  A=5 – number of cores
  B – number of hash-tables
  C – size of hash-table

## Slide 15: Testing – Output
Accuracy of HashPipe Algorithm (Errors False Negative and False Positive)
Average place of packets from HashPipe Alg’ in sorted list of Real "Heavy-Hitter" flows start from heaviest
  Optimal K = min(K, Number of HashPipe alg’ Flows, Number of Real “Heavy-hitter” Flows) – biggest number of “heavy-hitter” flows which we can check (not bigger than K)
  Optimal Average = (Optimal K + 1) / 2 – Average which we get for Accuracy=100%

## Slide 16: Example
Input: K = 3
Output:
Accuracy
Average
Optimal Average
HashPipe Alg’ Flows | Real Heavy-Hitter Flows
1 | 1
3 | 2
5 | 3
2 | 4
4 | 5

## Slide 17: Makefile
.PHONY: tcpdump tcpreplay result
tcpdump:
sudo tcpdump -B 262144 -l -xx -n -v -i vf0_1 > RealHeavyHitterFlows
tcpreplay:
sudo tcpreplay -L$(NUM) -i vf0_0 $(CAPTURE)
sudo /opt/netronome/bin/nfp-rtsym i32._sketch.108 > HashPipeFlows
sudo /opt/netronome/bin/nfp-rtsym i33._sketch.108 >> HashPipeFlows
sudo /opt/netronome/bin/nfp-rtsym i34._sketch.108 >> HashPipeFlows
sudo /opt/netronome/bin/nfp-rtsym i35._sketch.108 >> HashPipeFlows
sudo /opt/netronome/bin/nfp-rtsym i36._sketch.108 >> HashPipeFlows
result:
python getResult.py $(K)

## Slide 18
Chart: Accuracy, NUM = 100 000, Size = 5x12x128
| 1 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200
Accuracy, % | 100 | 96.5174 | 91.5212 | 89.5175 | 89.1386 | 87.013 | 83.2639 | 81.656 | 80.2623 | 80.5108 | 79.91 | 78.5552 | 76.718 | 75.3172 | 74.5805 | 72.076 | 69.7282 | 67.8918 | 66.2594 | 65.0618 | 63.5718 | 63.5718

## Slide 19
Chart: Average, NUM = 100 000, Size = 5x12x128
| 1 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400 | 3600 | 3800 | 4000 | 4200
Average | 0 | 100.7761 | 207.0125 | 318.0815 | 426.1011 | 556.9241 | 691.6944 | 827.5353 | 979.1462 | 1119.322 | 1267.1164 | 1458.9037 | 1697.2561 | 1894.461 | 2087.7676 | 2619.2779 | 3096.8472 | 3516.7498 | 3940.7648 | 4314.6832 | 4485.1142 | 4485.1142
Optimal Average | 1 | 101 | 201 | 301 | 401 | 501 | 601 | 701 | 801 | 901 | 1001 | 1101 | 1201 | 1301 | 1401 | 1501 | 1601 | 1701 | 1801 | 1901 | 1901.5 | 1901.5
Optimal K | 1 | 201 | 401 | 601 | 801 | 1001 | 1201 | 1401 | 1601 | 1801 | 2001 | 2201 | 2401 | 2601 | 2801 | 3001 | 3201 | 3401 | 3601 | 3801 | 3802 | 3802

## Slide 20: Conclusions
For NUM=100 000 packets and memory size 5x12x128 accuracy >60% for a big value of K such as 4000
As a result of the HashPipe Algorithm, we got less than 4000 packets, so for K more than 4000 the results will not change

## Slide 21
Chart: Accuracy, NUM = 100 000, K = 2000, Size = 5x12xC
| 12x2 | 12x4 | 12x8 | 12x16 | 12x32 | 12x64 | 12x128 | 12x256 | 12x512
Accuracy, % | 43.3962 | 52.5862 | 61.658 | 61.9898 | 67.11 | 64.922 | 79.5 | 87.7 | 93.3

## Slide 22
Chart: Average, NUM = 100 000, K = 2000, , Size = 5x12xC
| 12x2 | 12x4 | 12x8 | 12x16 | 12x32 | 12x64 | 12x128 | 12x256 | 12x512
Average | 598.4906 | 672.0259 | 772.9223 | 967.4592 | 1511.9855 | 2574.7806 | 1278.5745 | 1085.708 | 1024.2085
Optimal Average | 27 | 58.5 | 97 | 196.5 | 414 | 898.5 | 1000.5 | 1000.5 | 1000.5
Optimal K | 53 | 116 | 193 | 392 | 827 | 1796 | 2000 | 2000 | 2000

## Slide 23: Conclusions
Accuracy is highly dependent on memory size – for standard parameters (NUM=100 000 and K=2000):
  for memory size 5x12x4 – accuracy ≈52%
  for memory size 5x12x128 – accuracy ≈80%
  for memory size 5x12x512 – accuracy ≈93%
For good results, it is important that the memory size (number of places for different packages) be significantly larger than K

## Slide 24
Chart: Accuracy, NUM = 100 000, K = 2000, Size = 5xBxC
| 3x512 | 6x256 | 12x128 | 24x64 | 48x32 | 96x16 | 192x8 | 384x4
Accuracy, % | 60.1 | 73.85 | 79.35 | 80.4 | 81.35 | 79.65 | 79.4 | 76.15

## Slide 25
Chart: Average, NUM = 100 000, K = 2000, , Size = 5xBxC
| 3x512 | 6x256 | 12x128 | 24x64 | 48x32 | 96x16 | 192x8 | 384x4
Average | 2145.865 | 1521.3645 | 1280.4055 | 1261.9685 | 1224.882 | 1258.766 | 1292.5275 | 1416.658
Optimal Average | 1000.5 | 1000.5 | 1000.5 | 1000.5 | 1000.5 | 1000.5 | 1000.5 | 1000.5
Optimal K | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000 | 2000

## Slide 26: Conclusions
For constant memory size best results are achieved when the number of hash-tables and the hash-table size are approximately equal:
  for memory size 5x48x32 – accuracy ≈81%
And if one of the parameters is greatly reduced, then the results will deteriorate:
  for memory size 5x3x512 – accuracy ≈60%
  for memory size 5x384x4 – accuracy ≈76%

## Slide 27
Chart: Time
| 0 | 100000 | 200000 | 300000 | 400000 | 500000 | 600000 | 700000 | 800000 | 900000 | 1000000 | 1100000 | 1200000 | 1300000 | 1400000 | 1500000 | 1600000 | 1700000 | 1800000 | 1900000
Time | 0 | 0.24779 | 0.48356 | 0.70715 | 0.93006 | 1.1608 | 1.398 | 1.6376 | 1.8641 | 2.0856 | 2.3153 | 2.5424 | 2.7797 | 3.0233 | 3.2675 | 3.5061 | 3.7413 | 3.992 | 4.2422 | 4.4839

## Slide 28
Chart: Accuracy, K = 2000, Size = 5x12x128
| 2000 | 10000 | 100000 | 500000 | 1000000 | 2000000
Accuracy, % | 100 | 94.15 | 79.9 | 77.9 | 76.6 | 74.2

## Slide 29
Chart: Average, K = 2000, Size = 5x12x128
| 2000 | 10000 | 100000 | 500000 | 1000000 | 2000000
Average | 419 | 1054.093 | 1260.676 | 1371.2185 | 1411.7355 | 1500.273
Optimal Average | 420 | 1000.5 | 1000.5 | 1000.5 | 1000.5 | 1000.5
Optimal K | 839 | 2000 | 2000 | 2000 | 2000 | 2000

## Slide 30: Conclusions
For a large number of packets, we can assume that the graphs, depending on the number of packets, are identical to the graphs of the processing time of these packets
The number of sent (NUM) packets affects the results much weaker than K or memory size
But NUM strongly affects the execution time of the program.

## Slide 31: Learning
Learned to work with Netronome SmartNIC
Learned to use IDE Programmer Studio 6.0
Practiced writing code in the programming languages P4, C and Python
Practiced using console commands to work with traffic and with SmartNIC (tcpreplay, tcpdump, nfp-rtsym)

## Slide 32: Thanks for watching!